## Slide 1
03
Pthreads and
Performance Measurement
Counting what the hardware actually did — threads, counters, affinity, and the clock that will not sit still
CS-3006 Parallel and Distributed Computing · Fall 2026
Notes: Demo 01 of the course. Everything on these slides is run live from the pdc-demo-01-pthreads package.

## Slide 2
WHERE WE ARE
Three questions this lecture answers
1
Did it actually run in parallel?
Wall time alone cannot tell you. CPU-time / wall-time can, and hardware counters can say more.
2
Why did it stop getting faster?
Amdahl is only the first suspect. Cache coherence, core heterogeneity and clock throttling are the other three.
3
What can I control, and what merely happens to me?
Affinity, scheduling and frequency are all partly out of your hands — and differently so on Linux and on Apple Silicon.
Notes: Frame the whole demo. Come back to these three at the end.

## Slide 3
THE TARGET
The machine is not what the textbook drew
An 8-core Apple M1 is two different CPUs on one die.
4 × Firestorm
performance cores
wide out-of-order, large caches
high clock, high power
hw.perflevel0.logicalcpu
4 × Icestorm
efficiency cores
narrow, small caches, low clock
a fraction of the throughput
hw.perflevel1.logicalcpu
Consequence: your eighth thread does not add what your second thread added. That is not overhead — it is a different core.
A lab x86 box is uniform, but has SMT: two logical CPUs sharing one core's execution units. Same lesson, different mechanism — "logical CPU" is a promise of scheduling, not of throughput.
Notes: Run ./scripts/sysinfo.sh live here. On a lab machine show lscpu and point at Thread(s) per core.

## Slide 4
THE API
Pthreads is five function calls
#include <pthread.h>
void *worker(void *arg) {
task_t *t = (task_t *)arg;
t->result = compute(t->iters);
return NULL; // or pthread_exit(...)
}
pthread_t th[N];
for (int i = 0; i < N; i++)
pthread_create(&th[i], NULL, worker, &task[i]);
for (int i = 0; i < N; i++)
pthread_join(th[i], NULL); // blocks till it ends
Own stack
Locals are private. Everything reached through a pointer is not.
Shared heap & globals
One address space. This is the whole point, and the whole danger.
Argument passing
One void*. Give each thread its own struct — never a pointer to a loop variable.
Join before reading
Results are only guaranteed visible after pthread_join.
Notes: Live: ./bin/01_hello -t 4

## Slide 5
DEMO 01
Shared memory, shared bugs
Four threads. Each adds 1 to the same variable, 200 000 times.
800,000
expected
≈ 300,000
actually counted
800,000
with a mutex
counter++ is three instructions, not one:
ldr x0, [counter] // both cores read 7
add x0, x0, #1 // both compute 8
str x0, [counter] // both write 8 -> one update lost
The mutex restores correctness and destroys scalability. Both halves of that sentence get measured in demo 03.
Notes: Exact loss varies run to run — that non-determinism is itself the lesson.

## Slide 6
MEASUREMENT
Wall time tells you that. Counters tell you what.
cycles
hardware time actually spent
instructions
work that actually completed
IPC = instructions / cycles
how well the pipeline was fed — the best single health metric
ref-cycles
time at the invariant base clock; cycles/ref-cycles = the real turbo ratio
cache-misses
the currency of false sharing and bad access patterns
cpu-migrations
threads bouncing between cores; pinning should drive this to ~0
task-clock
CPU-milliseconds; ÷ elapsed = average cores kept busy
Low IPC + high cache-misses = memory. Low IPC + high context-switches = contention. Healthy IPC + falling clock = power and heat.
Notes: This slide is the vocabulary the rest of the course leans on.

## Slide 7
TOOLING
Reading the counters: same physics, different rules
Linux (your lab machines)
The PMU is open to user code.
perf_event_open() from inside the program, or perf stat around it.
Per-process, per-thread, exact.
perf stat -e cycles,instructions, \
ref-cycles,cache-misses,\
cpu-migrations ./bin/02_scaling
# if it refuses:
sudo sysctl -w \
kernel.perf_event_paranoid=1
macOS / Apple Silicon
The PMU is not exposed to user processes.
No perf. Counters come from Instruments; SoC telemetry from powermetrics.
# cycles, instructions, IPC
xctrace record \
--template 'CPU Counters' \
--launch -- ./bin/02_scaling
# cluster GHz, residency, watts
sudo powermetrics \
--samplers cpu_power -i 1000
Same physics, different permission model. Wrapped for you in scripts/linux_perf.sh, scripts/mac_xctrace.sh and scripts/mac_powermetrics.sh.
Notes: Be explicit that the Mac restriction is a permission decision, not a hardware limitation.

## Slide 8
DEMO 02
Strong scaling, and the ceiling
Chart: Speedup vs threads — expected shape on a base M1
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Ideal (linear) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Measured (4P + 4E) | 1 | 1.97 | 2.9 | 3.8 | 4.2 | 4.5 | 4.75 | 4.95
Illustrative shape, not measured data — run it on your own machine.
Amdahl's law
S(n) ≤ 1 / ( (1-p) + p/n )
p = 0.95 → ceiling of 20×, no matter how many cores.
But the bend at 4 threads here is not Amdahl at all — it is where the P-cores run out and the E-cores take over.
Fit Amdahl to a heterogeneous machine and you will "measure" a serial fraction that does not exist.
Notes: Live: ./bin/02_scaling -s 1.0. Ask the class to predict the bend before it prints.

## Slide 9
DEMO 03
Same instructions. Same arithmetic. Different address.
Four threads incrementing four counters. The only thing that changes is where those counters sit.
packed — one cache line
c0
c1
c2
c3
128 bytes — every store invalidates the line in all four L1s
padded — one line each
c0
c1
c2
c3
no line is ever shared — no coherence traffic at all
False sharing
The hardware's unit of sharing is a cache line, not a variable. Two cores writing to different variables in the same line still fight for exclusive ownership of it — tens of cycles per store, for data neither core shares.
atomic and mutex are TRUE sharing: the algorithm really does serialise. Padding cannot help — only per-thread partials with one reduction at the end.
Notes: Live: ./bin/03_false_sharing. Needs threads on distinct physical cores or the effect vanishes.

## Slide 10
128
bytes per cache line on Apple Silicon
Most x86-64 parts use 64. A struct padded with alignas(64) is correct on the lab machines and silently broken on an M-series Mac — two counters still share a line, and no unit test will ever notice.
$ ./bin/03_false_sharing --sweep
stride wall(s) Mupd/s
-----------------------------
8 2.041 39.2
16 1.988 40.2
32 1.502 53.3
64 0.883 90.6
128 0.121 661.2 <--
256 0.119 672.3
^ the line size, measured
Don't hard-code it. Measure it.
Notes: The stride sweep takes about ten seconds and is the most convincing thing in the demo.

## Slide 11
DEMO 04
Processor affinity: two different philosophies
Linux — control
cpu_set_t set;
CPU_ZERO(&set);
CPU_SET(3, &set);
pthread_attr_setaffinity_np(
&attr, sizeof(set), &set);
Hard pinning. That thread runs on CPU 3 and nowhere else.
Migrations → 0, caches stay warm, variance drops.
You can also get it badly wrong.
Apple Silicon — influence
// no pthread_setaffinity_np here
pthread_attr_set_qos_class_np(
&attr, QOS_CLASS_USER_INITIATED, 0);
// -> P cluster
// QOS_CLASS_BACKGROUND -> E only
THREAD_AFFINITY_POLICY still compiles and is refused by the kernel.
You state intent; the scheduler decides.
You cannot get it badly wrong either.
Portable code must not depend on either. Ask for what you need; measure what you got.
Notes: Live: ./bin/04_affinity -s 1.0. The kern_return_t refusal prints first.

## Slide 12
DEMO 04
A core is not a core
Chart: Relative per-thread throughput — expected shape
| 1 thr, P cluster | 1 thr, E cluster | 4 thr on P | 4 thr on E | 8 thr default
per-thread throughput (Miter/s) | 100 | 34 | 96 | 33 | 62
Illustrative shape, not measured data.
The P/E ratio is roughly 3×.
A hot thread that lands on an efficiency core costs you that — and nothing in your code is told.
Default QoS lands in between.
The scheduler spreads across both clusters, so the average thread is neither fast nor slow.
Oversubscription adds nothing.
For a compute-bound kernel, 16 threads on 8 cores halves every thread and moves the total not at all.
Notes: Ask: which of these would a naive OpenMP num_threads(8) give you?

## Slide 13
DEMO 05
The clock will not sit still
Chart: Sustained load: throughput (%) vs seconds — expected shape
| 1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40
single-thread throughput | 100 | 100.4 | 99.8 | 98.1 | 95.2 | 92.6 | 90.9 | 89.8 | 89.3 | 89.1 | 89
Illustrative shape, not measured data. A fanless MacBook Air shows this far more sharply than a MacBook Pro.
Two independent effects
Over time — the boost budget is spent and the die heats up. Same thread, same code, slower.
Over cores — waking more cores lowers the frequency every core can hold. Your 8-thread run is not 8 copies of your 1-thread run.
Both look like "my parallel code scaled badly" in wall time alone.
Notes: Run ./bin/05_frequency -d 30 with sudo ./scripts/mac_powermetrics.sh in a second window.

## Slide 14
DEMO 05
"Overclocking", then and now
Then
A fixed clock with headroom left on the table.
Raise the multiplier, add voltage, add cooling, gain 20–30%.
The chip did exactly what the multiplier said.
The risk was yours: instability, heat, a dead part.
Now
A closed control loop over power, temperature and active-core count.
The part already runs as fast as those limits allow, millisecond by millisecond.
x86 desktop: firmware still exposes multipliers; the OS can toggle turbo.
Apple Silicon: no multiplier, no voltage offset, no BIOS. Nothing to raise.
So the question changed: not "how fast can I make it go" but "what did it actually run at, and what made it choose that" — and that one you can answer, on any machine, with counters.
Notes: The safe A/B on Linux is scripts/linux_freq.sh: change the governor's target, measure, restore. It never raises a vendor limit.

## Slide 15
HANDS ON
The safe experiment on a lab machine
$ ./scripts/linux_freq.sh show # governor, driver, limits, turbo state
$ sudo ./scripts/linux_freq.sh ab ./bin/02_scaling -s 1.0 -t 1
governor=performance boost=1 -> cycles/ref-cycles = 1.42
governor=performance boost=0 -> cycles/ref-cycles = 1.00
governor=powersave boost=1 -> cycles/ref-cycles = 0.61
(restores your original governor on exit)
We change the target, never the limit.
cycles / ref-cycles is the real multiplier — read it, don't assume it.
Firmware-level overclocking voids warranties and has no place on a shared machine.
Notes: On the Mac the equivalent A/B is Low Power Mode on/off, plus battery vs mains.

## Slide 16
THE LAB
Run it yourself
$ make
$ ./scripts/sysinfo.sh # what machine am I on?
$ ./scripts/run_all.sh # every demo, CSVs into results/
01_hello
create/join, a real race, the mutex fix
02_scaling
speedup, efficiency, IPC, effective clock
03_false_sharing
packed vs padded, and a stride sweep that finds your cache line
04_affinity
P vs E cores on macOS; pinning and SMT on Linux
05_frequency
sustained load, DVFS, and what you may actually change
Deliverable: filled-in tables, answers to Q1–Q9, one speedup plot, and two paragraphs on the largest loss you measured. Compare with someone on a different machine — the shapes should agree even where the numbers don't.
Notes: Handout: handout/PDC-Lab01-Handout.md

## Slide 17
What to carry forward
1
Measure, don't assume.
Wall time says something is slow. Counters say what kind of slow.
2
The unit of sharing is a cache line.
Not a variable. Padding is a correctness concern for performance.
3
A logical CPU is a scheduling promise, not a throughput promise.
P-cores, E-cores and SMT siblings all count as "a CPU".
4
Frequency is an output, not an input.
The chip picks it from power, heat and how many cores are awake.
5
Portability is about what you ask for, not what you get.
State intent, then verify — on both operating systems.
Next: OpenMP — the same measurements, a fraction of the code.
Notes: Close by returning to the three questions from slide 2.